## Slide 1: Device Identification using wireless technologies
Ryan parkins

## Slide 2: Bluetooth low energy (BLE)
Low energy version of Bluetooth, for small amounts of data e.g. sensor data
Usually found in smartwatches and other IOT
2.4GHz Frequency
< 100m Range

## Slide 3: Connection handling
Standby - Device is powered off and not transmitting
Advertising - Device is advertising itself out to all nearby devices, it is also listening for responses
Scanning - Device is listening to all packets sent over all channels, used to scan for devices
Initialising - State a central device enters before a connection is established to peripherals (Waiting for connection(s) to be made)

## Slide 4
Advertising state
A BLE device enters an advertising state whilst it is not connected to a peripheral device and is powered on
Information is transmitted out to any nearby device that is listening (scanning state)
Data transmitted includes
  MAC address
  Device name
scanning state
Scanning state listens out for all nearby devices
Can obtain nearby MAC addresses with associated device names

## Slide 5: So how can this be of use?

## Slide 6: Device presence detection
By using a device in the “scanning” state, we can analyse all nearby advertising data, this means that a list of all nearby MAC addresses can be gathered from a BLE scan

## Slide 7: Unique devices
By analysing MAC addresses, not only can the number of devices be seen, but also a record of addresses can be stored
By storing addresses, we can compare MAC’s of nearby devices and those previously seen
This will allow us to differentiate between devices and monitor their presence

## Slide 8: Development
Written in python - Linux

## Slide 9: Libraries used
Bluetooth (Discovery Service) – Used for performing the BLE scan
Matplotlib – Used to display the results in a live, updating graph

## Slide 10: What does this look like in action?

## Slide 11
Number of devices in range
Unique devices, Each MAC address given a unique ID
Unique devices, Time in seconds

## Slide 12: GitHub repository